## Slide 1
Line of Fire Program
Electrical Equipment & Exposure Activity Package

## Slide 2
Purpose
To raise awareness and reduce the risk of injury or fatality associated with exposure to electrical energy by:
improving hazard recognition,
safe work practices, and
effective controls when working with or near electrical equipment.

## Slide 3
Why it Matters
Electrical hazards can result in:
Electric shock or electrocution
Arc flash and arc blast injuries
Burns, fires, and explosions
Secondary injuries (falls, dropped objects, line-of-fire events)
Electrical incidents often occur during maintenance, troubleshooting, temporary power use, and equipment modification, especially when controls are bypassed or conditions change.

## Slide 4
Scope
This activity package applies to:
Fixed and portable electrical equipment
Temporary power systems
Energized systems and components
Work conducted by qualified and non-qualified workers
All operational, construction, and maintenance activities where electrical exposure exists

## Slide 5
Common Electrical Hazards
Contact with energized conductors or terminals
Damaged cords, plugs, or insulation
Inadequate grounding or bonding
Improper use of extension cords or power bars
Moisture, conductive dust, or corrosive environments
Overloaded circuits
Arc flash from switching, fault conditions, or improper tools
Working within restricted approach boundaries

## Slide 6
LoF Injury reduction campaign
You are in the line of fire when you are at risk of coming into contact with a force your body cannot endure.
Electrical awareness is:
Stored Energy Contact with stored energy Includes pressure releases
Striking Hazards Struck by or striking against an object Includes dropped objects
Crushing Hazards Caught in, on or between an object Includes hand injuries

## Slide 7
This overview includes materials that relate to the Line of Fire Life Saving Rule and some that do not. The Life Saving Rule focuses on body positioning.
This rule indicates:
Keep yourself and others out of the line of fire
I position myself to avoid:
  Moving objects
  Vehicles
  Pressure releases
  Dropped objects
I establish and obey barriers and exclusion zones
I take action to secure loose objects and report potential dropped objects
Line of Fire Life Saving Rule

## Slide 8
Related Life Saving Rules
FIT FOR DUTY
BYPASSING SAFETY CONTROLS
ENERGY ISOLATION
WORK AUTHORIZATION

## Slide 9
High-Risk Tasks & Activities
Potential Consequences
Examples | Potential Consequences
Equipment inspection, testing, and troubleshooting Lockout/tagout (LOTO) not properly applied or verified Use of temporary power during shutdowns or turnarounds Working near overhead or buried power lines Connecting or disconnecting energized equipment Use of non-rated tools or PPE Bypassing interlocks or protective devices | Serious injury or fatality Fire or explosion Equipment damage and unplanned downtime Regulatory non-compliance Environmental and reputational impacts

## Slide 10
Required Controls (Hierarchy of Controls)
Elimination & Engineering Controls
De-energize equipment whenever feasible
Design systems to minimize energized work
Use ground-fault circuit interrupters (GFCIs)
Install arc-resistant equipment and barriers
Clearly label electrical panels and circuits

## Slide 11
Required Controls (Hierarchy of Controls)
Administrative Controls
Electrical hazard assessments and job planning
Permit-to-work for energized tasks
Lockout/Tagout procedures with verification
Only qualified and authorized people perform electrical work
Clear signage and restricted access zones
Pre-job safety meetings and task-specific hazard analysis
PPE (Last Line of Defense)
Arc-rated clothing appropriate to incident energy
Voltage-rated gloves with leather protectors
Face shields, balaclavas, and safety glasses
Insulated tools and mats
CSA-approved footwear

## Slide 12
Responsibilities
Workers
Follow electrical safety procedures and permits
Never assume equipment is de-energized—test before touch
Inspect tools, cords, and PPE before use
Stop work and report unsafe conditions immediately
Supervisors
Ensure workers are trained and competent
Verify permits, LOTO, and hazard controls
Reinforce safe behaviors and intervene when required
Ensure equipment is maintained and compliant
Management
Provide resources, training, and leadership commitment
Ensure compliance with applicable codes and standards
Support a culture where stopping unsafe work is encouraged

## Slide 13
Warning Signs & Red Flags
Missing or damaged electrical covers
Exposed conductors or temporary wiring
Tripped breakers or blown fuses repeatedly
Unlabeled panels or unclear isolation points
Moisture around electrical equipment
people unsure of voltage levels or boundaries

## Slide 14
Field Verification: IOGP Questions & Actions
Hazard Prevention Questions | Prevention Actions
Have you verified zero energy and that isolation (lock out tag out) is in place and effective? E.g., test before touch. Do you know and maintain the safe distance from overhead or underground powerlines to avoid contact or potential for arcing? Are effective controls in place, when servicing energized equipment, or when switching a breaker into position? E.g., anti static/arc rated PPE, grounding/earthing mats. Do you consider your positioning when working on energized equipment, in relation to the equipment movement as well as the power source? Is access to electrical rooms, panels, switch gear, etc. restricted to authorized personnel only? | Zero Energy Check: Verify zero energy and effectiveness of isolation (lock out tag out), test before touch. Powerlines - Maintain Safe Distance: Know and maintain the safe distance from overhead or underground powerlines to avoid contact or potential for arcing. Energized Equipment: integrate effective controls when servicing energized equipment or when switching a breaker into position. E.g., anti static/arc rated PPE, grounding/earthing mats. Safe Positioning: Consider your positioning when working on energized equipment, in relation to the equipment movement as well as the power source. Restricted Access: Limit access to electrical rooms, panels, and switch gear to authorized personnel.
Visit this link for more information: Life-Saving Rules | IOGP
Scroll down to see the publication on Line of Fire

## Slide 15
New Concepts
Review applicable concepts and apply as necessary (see Attachment B for more details):
 | Concept | Description | Applicable? | Comment
1 | Energy Wheel | It is a visual tool used in safety management to help identify, categorize and manage hazards based on the types of energy present in the workplace. It simplifies the hazard recognition process by focusing on the various energy sources that could cause harm if not properly controlled. | Yes | 
2 | Hierarchy of Control | It is a systematic approach used to eliminate or minimize hazards associated with energy sources in the workplace. Part of safety management systems, it is commonly applied in industries where people may be exposed to hazardous energy during the operation, maintenance or servicing of equipment. | Yes | 

## Slide 16
New Concepts
Review applicable concepts and apply as necessary (see Attachment B for more details):
 | Concept | Description | Applicable? | Comment
3 | Stuff That Can Kill You (STCKY) | "Stuff that can kill you" (STCKY) is a safety concept used to identify and manage hazards or conditions in the workplace that pose a significant risk of serious injury or fatality. It emphasizes the importance of recognizing high-risk elements in work environments, which can cause life-threatening, life-altering or life-ending incidents if not properly controlled. | Yes | 
4 | Critical Work | Critical work refers to tasks or activities in a workplace that involve significant risk to people, property or the environment. These tasks often require precise planning, specialized skills and strict safety measures due to the potential for severe consequences if something goes wrong. In essence, critical work involves critical steps with inherent critical risks that could only be managed by critical controls. | Yes | 

## Slide 17
New Concepts
Review applicable concepts and apply as necessary (see Attachment B for more details):
 | Concept | Description | Applicable? | Comment
5 | Direct Control | This refers to the proactive and hands-on supervision, intervention and management of work activities to ensure safety standards and protocols are strictly followed. It involves real-time oversight by competent personnel to minimize risks and immediately address any unsafe conditions or behaviours. Direct Controls work even if people make errors. | Yes | Alternative Controls are specifically designed to mitigate human error. When a Direct Control is not feasible, there must be at least two Alternative Controls, from at least two or more of the available categories.
6 | High Energy Control Assessment (HECA) | HECA, also known as energy-based observation, is a structured process used to identify, evaluate and control risks associated with high-energy activities in the workplace. These activities involve significant energy sources — such as mechanical, electrical, chemical or thermal energies — that have the potential to cause catastrophic injuries or damage. HECA ensures that organizations assess and integrate robust controls to manage these risks effectively. | Yes | 

## Slide 18
Questions & Additional Verifications
Questions
What electrical hazards are present in today’s task?
Can the work be completed de-energized?
Do we know the correct isolation and verification points?
Are we using the correct PPE for the exposure?
What would cause an arc flash in this scenario?
Additional Verification Checklist
Electrical hazard assessment completed
Equipment de-energized where possible
Lockout/Tagout applied and verified
Qualified people assigned
Correct PPE and insulated tools in use
Work area controlled and communicated

## Slide 19
Final Thoughts
Key Takeaways
Electrical energy is silent, fast, and unforgiving
Most electrical incidents are preventable
De-energization is the safest option
Qualification, planning, and verification save lives
If unsure—stop, ask, and reassess