## Slide 1
Line of Fire Program
Projectiles/Explosion/Jet Fire Activity Package

## Slide 2
Purpose
To raise awareness and improve
hazard recognition,
risk assessment, and
control of projectile, explosion, and jet fire hazards
that can place people in the Line of Fire, potentially resulting in serious injury or fatality.

## Slide 3
Hazard Description
Projectiles
Objects that are forcefully ejected due to pressure release, mechanical failure, stored energy, or explosive forces. These can travel at high velocity and cause severe injuries.
Explosion
A rapid release of energy causing a blast wave, heat, noise, and flying debris. Explosions may result from flammable gas/vapour ignition, dust, chemical reactions, or pressure vessel failure.
Jet Fire
A high-velocity, pressurized release of flammable gas or liquid that ignites, producing intense heat, flame impingement, and radiant heat exposure.

## Slide 4
Why This Matters
People may underestimate stored energy and pressure-related hazards
Events often occur suddenly and without warning
Consequences include fatal injuries, burns, structural damage, and secondary fires
These hazards are commonly linked to maintenance, startup, shutdown, and abnormal operations

## Slide 5
Common Sources of Hazards
Projectiles
Pressurized hoses, fittings, valves, or caps
Ruptured pipes or pressure vessels
Tools or components under tension
Failed rotating or reciprocating equipment
Improperly secured equipment or components
Explosion
Gas leaks in confined or enclosed spaces
Ignition of flammable vapours or dust
Over-pressurized vessels or piping
Hot work near flammable atmospheres
Inadequate purging or isolation
Jet Fire
High-pressure gas or liquid hydrocarbon leaks
Flange, gasket, or valve failures
Corrosion or erosion under insulation (CUI)
Improper isolation during maintenance
Impact damage to pressurized lines

## Slide 6
LoF Injury reduction campaign
You are in the line of fire when you are at risk of coming into contact with a force your body cannot endure.
Projectiles/Explosion/Jet Fire awareness is:
Stored Energy Contact with stored energy Includes pressure releases
Striking Hazards Struck by or striking against an object Includes dropped objects
Crushing Hazards Caught in, on or between an object Includes hand injuries

## Slide 7
This overview includes materials that relate to the Line of Fire Life Saving Rule and some that do not. The Life Saving Rule focuses on body positioning.
This rule indicates:
Keep yourself and others out of the line of fire
I position myself to avoid:
  Moving objects
  Vehicles
  Pressure releases
  Dropped objects
I establish and obey barriers and exclusion zones
I take action to secure loose objects and report potential dropped objects
Line of Fire Life Saving Rule

## Slide 8
Related Life Saving Rules
FIT FOR DUTY
BYPASSING SAFETY CONTROLS
ENERGY ISOLATION
WORK AUTHORIZATION

## Slide 9
Key Line of Fire Exposures
Potential Consequences
Examples | Potential Consequences
Standing in front of pressurized components Working near flanges, valves, or pressure relief points Conducting maintenance without full isolation Remaining in blast radius or flame impingement zones Inadequate barricading or exclusion zones | Fatal or life-altering injuries Severe burns and blast injuries Structural damage and equipment loss Escalation to major incidents Environmental release Operational downtime

## Slide 10
Controls and Prevention Measures
Engineering Controls
Pressure relief devices and burst discs
Blast-resistant design and shielding
Fixed gas detection and alarms
Fire and gas (F&G) systems
Remote isolation valves
Proper pressure rating of equipment
Administrative Controls
Hazard identification and risk assessments (e.g., JSA/JHA)Permit to Work (PTW) systems
Lockout/Tagout and energy isolation process designs
Management of Change (MOC)Equipment inspection and maintenance programs
Clear exclusion and barricaded zones
Consider Direct or Alternative Controls

## Slide 11
Safeguards & Preventive Measures
Safe Work Practices
Verify zero energy before work begins
Never loosen fittings under pressure
Maintain safe distances from pressurized systems
Follow startup and shutdown process designs
Use leak detection methods safely
Stop work if conditions change or safeguards fail
PPE (Last Line of Defense)
Flame-resistant (FR) clothing
Face shields and eye protection
Gloves appropriate for pressure and chemical hazards
Hearing protection
Respiratory protection (where required)

## Slide 12
What Signs to Watch for
Unexpected pressure readings
Vibrations, rattling, or unusual noises
Smell of gas or hydrocarbons
Not using gas monitoring devices (fixed or personal)
Visible leaks, misting, or vapour clouds
Corrosion, bulging, or damaged piping
Alarms or abnormal operating conditions

## Slide 13
What to do if a hazard is identified
Stop work immediately
Move to a safe location
Isolate energy sources if trained and authorized
Raise the concern to supervision
Follow site emergency response process designs
Do not attempt temporary fixes on pressurized systems

## Slide 14
Responsibilities
Workers
Stay out of the Line of Fire
Challenge unsafe conditions
Follow process designs and permits
Report near misses and unsafe conditions
Leaders
Ensure hazards are discussed during planning
Reinforce Line of Fire awareness
Verify safeguards are in place before work begins
Support stop-work authority

## Slide 15
Field Verification: IOGP Questions & Actions
Hazard Prevention Questions | Prevention Actions
Can people and combustible materials be kept out of the line of fire during tasks in the workplace that generate sparks, flying debris, or projectiles? E.g., grinding, chipping, abrasive blasting, hydro-blasting, pigging, etc. Are effective safeguards in place to protect personnel from exposure to explosion/projectiles? E.g., barricade and restrict access, area containment, blast walls. Are safe pathways and shelter-in-place available, known, and their use practiced, in case of explosion or jet fire? Has hot work been adequately controlled, including gas test if required? | Flying Debris: Keep people out of the line of fire during tasks like grinding, chipping, or blasting, that may create projectiles. Protection from Projectiles and Explosions: Use barricades and safeguards to protect personnel from exposure and/or restrict access. Protection from Jet Fires: Make sure safe pathways and shelter-in-place are available, known, and their use practiced. Hot Work: Ensure adequate safeguards are in place, including gas test if required.
Visit this link for more information: Life-Saving Rules | IOGP
Scroll down to see the publication on Line of Fire

## Slide 16
New Concepts
Review applicable concepts and apply as necessary (see Attachment B for more details):
 | Concept | Description | Applicable? | Comment
1 | Energy Wheel | It is a visual tool used in safety management to help identify, categorize and manage hazards based on the types of energy present in the workplace. It simplifies the hazard recognition process by focusing on the various energy sources that could cause harm if not properly controlled. | Yes | 
2 | Hierarchy of Control | It is a systematic approach used to eliminate or minimize hazards associated with energy sources in the workplace. Part of safety management systems, it is commonly applied in industries where people may be exposed to hazardous energy during the operation, maintenance or servicing of equipment. | Yes | 

## Slide 17
New Concepts
Review applicable concepts and apply as necessary (see Attachment B for more details):
 | Concept | Description | Applicable? | Comment
3 | Stuff That Can Kill You (STCKY) | "Stuff that can kill you" (STCKY) is a safety concept used to identify and manage hazards or conditions in the workplace that pose a significant risk of serious injury or fatality. It emphasizes the importance of recognizing high-risk elements in work environments, which can cause life-threatening, life-altering or life-ending incidents if not properly controlled. | Yes | 
4 | Critical Work | Critical work refers to tasks or activities in a workplace that involve significant risk to people, property or the environment. These tasks often require precise planning, specialized skills and strict safety measures due to the potential for severe consequences if something goes wrong. In essence, critical work involves critical steps with inherent critical risks that could only be managed by critical safeguards. | Yes | 

## Slide 18
New Concepts
Review applicable concepts and apply as necessary (see Attachment B for more details):
 | Concept | Description | Applicable? | Comment
5 | Direct Control | This refers to the proactive and hands-on supervision, intervention and management of work activities to ensure safety standards and protocols are strictly followed. It involves real-time oversight by competent personnel to minimize risks and immediately address any unsafe conditions or behaviours. Direct Controls work even if people make errors. | Yes | Alternative Controls are specifically designed to mitigate human error. When a Direct Control is not feasible, there must be at least two Alternative Controls, from at least two or more of the available categories.
6 | High Energy Control Assessment (HECA) | HECA, also known as energy-based observation, is a structured process used to identify, evaluate and control risks associated with high-energy activities in the workplace. These activities involve significant energy sources — such as mechanical, electrical, chemical or thermal energies — that have the potential to cause catastrophic injuries or damage. HECA ensures that organizations assess and integrate robust safeguards to manage these risks effectively. | Yes | 

## Slide 19
Discussion Questions
Questions
Where could projectile, explosion, or jet fire hazards exist in our work today?
What energy sources are present and how are they controlled?
Are exclusion zones clearly defined and respected?
What would we do if a leak or pressure release occurred?
Key Takeaway
Pressure, energy, and flammable materials can turn routine tasks into catastrophic events. Recognize the hazard, control the energy, and keep yourself and others out of the Line of Fire.