## Slide 1
Line of Fire Program
Tensioned Lines/Spring Loaded Devices/Stored Energy Activity Package

## Slide 2
Hazard Overview
Stored energy hazards exist when energy is accumulated and held in a system that can be released suddenly and without warning. When released, this energy can strike, crush, cut, or entangle people—placing them directly in the line of fire.
Common forms include:
Tensioned or loaded lines
Springs and spring-loaded mechanisms
Hydraulic or pneumatic pressure
Gravity-stored energy
Mechanical and rotational energy
Uncontrolled energy release has resulted in serious injuries and fatalities across construction, energy, maintenance, and industrial operations.

## Slide 3
Why it Matters
When stored energy is released:
The movement is fast, forceful, and unpredictable
Escape time is minimal or nonexistent
Injuries are often severe (fractures, amputations, fatalities)
Key Risk Reality:
If you are in the snap-back zone or pinch point, PPE will not protect you.

## Slide 4
Common Sources of Stored Energy
Tensioned Lines
Wire rope, chains, slings under load
Winch lines, tugger lines
Guy wires, tag lines under tension
Tow straps, ratchet straps
Spring-Loaded Devices
Valve actuators
Counterweights
Mechanical latches and clamps
Garage-style doors, hatches, or covers
Pressurized tool components
Stored Energy Systems
Hydraulic cylinders and hoses
Pneumatic lines and air receivers
Pressurized vessels
Suspended or elevated loads
Rotating equipment components

## Slide 5
LoF Injury reduction campaign
You are in the line of fire when you are at risk of coming into contact with a force your body cannot endure.
Tensioned Lines/Spring Loaded Devices/Stored Energy awareness is:
Stored Energy Contact with stored energy Includes pressure releases
Striking Hazards Struck by or striking against an object Includes dropped objects
Crushing Hazards Caught in, on or between an object Includes hand injuries

## Slide 6
This overview includes materials that relate to the Line of Fire Life Saving Rule and some that do not. The Life Saving Rule focuses on body positioning.
This rule indicates:
Keep yourself and others out of the line of fire
I position myself to avoid:
  Moving objects
  Vehicles
  Pressure releases
  Dropped objects
I establish and obey barriers and exclusion zones
I take action to secure loose objects and report potential dropped objects
Line of Fire Life Saving Rule

## Slide 7
Related Life Saving Rules
FIT FOR DUTY
BYPASSING SAFETY CONTROLS
ENERGY ISOLATION
WORK AUTHORIZATION
SAFE MECHANICAL LIFTING

## Slide 8
Line of Fire Scenarios
Potential Consequences
People may be exposed when: | Potential Consequences
Standing in the snap-back zone Adjusting or disconnecting pressurized systems Releasing restraints or locking mechanisms Working beneath suspended loads Performing maintenance without full energy isolation Ask: “If this energy is released, where will it travel—and am I standing there?” | Struck-by or caught-between injuries Amputations or crush injuries Eye and facial trauma Fatal blunt force injuries Equipment damage and secondary incidents

## Slide 9
Required Controls (Hierarchy of Controls)
Elimination & Engineering Controls
Design systems to minimize stored energy
Use energy-dampening devices or guards
Install pressure relief valves and locking devices
Use remote tensioning or release mechanisms where possible

## Slide 10
Required Controls (Hierarchy of Controls)
Administrative Controls
Identify stored energy hazards during hazard assessments
Develop and follow energy isolation and release process designs
Use permits (LOTO, lifting, maintenance) as required
Clearly mark snap-back and exclusion zones
Ensure competent supervision during high-risk tasks
Consider Direct or Alternative Controls
Safe Work Practices
Never stand in the line of tension or snap-back path
Release energy slowly and in a controlled manner
Verify zero energy state before work begins
Maintain safe distances and use barriers
Communicate clearly before tensioning or releasing systems

## Slide 11
Required Controls (Hierarchy of Controls)
PPE (Last Line of Defense and does not prevent energy release.)
May include:
Eye and face protection
Cut-resistant gloves
Head protection
Task-specific PPE as identified in hazard assessment
Arc-rated clothing appropriate to incident energy

## Slide 12
Field-Level “Stope & Think” Questions
Before starting work:
What energy is stored in this system?
How could it be released unintentionally?
Where is the line of fire or snap-back zone?
Have all energy sources been isolated and verified?
Who is responsible for controlling the release?

## Slide 13
Responsibilities
Leaders/Supervisors
Leaders should:
Ensure energy hazards are identified in planning
Confirm isolation process designs are understood and followed
Challenge unsafe positioning and behaviours
Stop work if energy safeguard is unclear
Reinforce lessons learned from past incidents

## Slide 14
Field Verification: IOGP Questions & Actions
Hazard Prevention Questions | Prevention Actions
Are you aware of, and stay clear of, tensioned lines (e.g., chain, cable, mooring line, rope), strapping, coiled tubing, and coiled or spring-loaded devices? Are your hands and body clear of rigging equipment? E.g., cables and shackles. Have you considered the potential for pipe/equipment/sheeting movement when cutting, unbolting, or releasing items under tension or compression? Have you established exclusion/red zones where there is a potential for stored energy release? E.g., ‘snap back’ zones. | Positioning: Stay clear of tensioned lines (chains, cables, mooring lines, ropes), strapping, coiled tubing, and spring-loaded devices. Hands/Body Placement: Keep hands and body away from rigging, cables, and shackles. Pipe/Equipment Movement: Prepare for movement when cutting or unbolting, or release of stored energy. Exclusion/Red Zones: Establish exclusion/red zones where there is a potential for stored energy release. E.g., ‘snap back’ zones.
Visit this link for more information: Life-Saving Rules | IOGP
Scroll down to see the publication on Line of Fire

## Slide 15
New Concepts
Review applicable concepts and apply as necessary (see Attachment B for more details):
 | Concept | Description | Applicable? | Comment
1 | Energy Wheel | It is a visual tool used in safety management to help identify, categorize and manage hazards based on the types of energy present in the workplace. It simplifies the hazard recognition process by focusing on the various energy sources that could cause harm if not properly controlled. | Yes | 
2 | Hierarchy of Control | It is a systematic approach used to eliminate or minimize hazards associated with energy sources in the workplace. Part of safety management systems, it is commonly applied in industries where people may be exposed to hazardous energy during the operation, maintenance or servicing of equipment. | Yes | 

## Slide 16
New Concepts
Review applicable concepts and apply as necessary (see Attachment B for more details):
 | Concept | Description | Applicable? | Comment
3 | Stuff That Can Kill You (STCKY) | "Stuff that can kill you" (STCKY) is a safety concept used to identify and manage hazards or conditions in the workplace that pose a significant risk of serious injury or fatality. It emphasizes the importance of recognizing high-risk elements in work environments, which can cause life-threatening, life-altering or life-ending incidents if not properly controlled. | Yes | 
4 | Critical Work | Critical work refers to tasks or activities in a workplace that involve significant risk to people, property or the environment. These tasks often require precise planning, specialized skills and strict safety measures due to the potential for severe consequences if something goes wrong. In essence, critical work involves critical steps with inherent critical risks that could only be managed by critical safeguards. | Yes | 

## Slide 17
New Concepts
Review applicable concepts and apply as necessary (see Attachment B for more details):
 | Concept | Description | Applicable? | Comment
5 | Direct Control | This refers to the proactive and hands-on supervision, intervention and management of work activities to ensure safety standards and protocols are strictly followed. It involves real-time oversight by competent personnel to minimize risks and immediately address any unsafe conditions or behaviours. Direct Controls work even if people make errors. | Yes | Alternative Controls are specifically designed to mitigate human error. When a Direct Control is not feasible, there must be at least two Alternative Controls, from at least two or more of the available categories.
6 | High Energy Control Assessment (HECA) | HECA, also known as energy-based observation, is a structured process used to identify, evaluate and control risks associated with high-energy activities in the workplace. These activities involve significant energy sources — such as mechanical, electrical, chemical or thermal energies — that have the potential to cause catastrophic injuries or damage. HECA ensures that organizations assess and integrate robust safeguards to manage these risks effectively. | Yes | 

## Slide 18
Learning from Incidents
Many serious incidents occur because:
Stored energy was underestimated
Energy isolation was assumed, not verified
People relied on experience instead of process design
Changes were made without reassessing hazards
Lesson Learned:
Stored energy does not forgive assumptions.