## Slide 1
Line of Fire Program
Moving Vehicles/Mobile Equipment Activity Package

## Slide 2
Purpose
To reduce the risk of serious injury or fatality resulting from contact with moving vehicles or powered mobile equipment by:
increasing hazard awareness,
strengthening safeguards, and
reinforcing safe work behaviours.

## Slide 3
Why it Matters
Incidents involving mobile equipment are consistently among the highest-risk line of fire events in energy and industrial operations. These incidents often occur when:
People are struck, run over, pinned, or crushed
Visibility is limited or traffic safeguards are ineffective
Roles and communication between operators and ground workers are unclear
Key Message:
If you can’t see the operator, the operator can’t see you.

## Slide 4
Hazard Description
Moving vehicle and mobile equipment hazards exist whenever powered or self-propelled equipment is operating, including:
Trucks, loaders, excavators, forklifts, graders
Light-duty vehicles in work zones
Cranes, telehandlers, and specialized equipment
Common exposure scenarios:
Working on foot near operating equipment
Backing or turning movements
Congested or shared workspaces
Poor ground conditions or weather impacts

## Slide 5
LoF Injury reduction campaign
You are in the line of fire when you are at risk of coming into contact with a force your body cannot endure.
Moving object/vehicles/mobile equipment awareness is:
Stored Energy Contact with stored energy Includes pressure releases
Striking Hazards Struck by or striking against an object Includes dropped objects
Crushing Hazards Caught in, on or between an object Includes hand injuries

## Slide 6
This overview includes materials that relate to the Line of Fire Life Saving Rule and some that do not. The Life Saving Rule focuses on body positioning.
This rule indicates:
Keep yourself and others out of the line of fire
I position myself to avoid:
  Moving objects
  Vehicles
  Pressure releases
  Dropped objects
I establish and obey barriers and exclusion zones
I take action to secure loose objects and report potential dropped objects
Line of Fire Life Saving Rule

## Slide 7
Related Life Saving Rules
FIT FOR DUTY
DRIVING
SAFE MECHANICAL LIFTING
WORK AUTHORIZATION

## Slide 8
High-Risk Situations
Potential Consequences
Watch out for: | Potential Consequences
Reversing or blind-spot movements Equipment operating near structures, trenches, or edges People entering exclusion zones Simultaneous operations (SIMOPS) Night work, fog, snow, or dusty conditions Unplanned pedestrian access to equipment areas | Fatalities Crushing injuries Amputations Severe musculoskeletal injuries Property damage and operational shutdowns

## Slide 9
Required Controls (Hierarchy of Controls)
Elimination / Substitution
Remove pedestrian access where possible
Use remote or automated systems
Redesign workflows to separate people and equipment
Engineering Controls
Physical barriers and exclusion zones
Proximity detection or collision avoidance systems
Cameras, mirrors, and audible alarms
Clearly marked traffic routes and crossings

## Slide 10
Required Controls (Hierarchy of Controls)
Administrative Controls
Traffic management plans
Spotter requirements and protocols
Standardized hand signals and radio communication
Pre-job hazard assessments and field-level risk assessments
SIMOPS coordination and permits
Consider Direct or Alternative Controls
PPE (Last Line of Defense)
High-visibility clothing appropriate to the environment
CSA-approved head, eye, and foot protection
Weather-appropriate PPE that does not reduce visibility

## Slide 11
Responsibilities
Workers
Maintain eye contact with operators before approaching equipment
Stay out of exclusion zones unless authorized
Never assume an operator sees you
Use designated walkways and crossings
Stop work if conditions change or safeguards fail
Operators
Conduct pre-use inspections
Understand equipment blind spots
Stop operations if visibility is compromised
Confirm communication with spotters and ground workers
Follow site traffic rules at all times
Supervisor/Leaders
Reinforce separation of people and equipment
Ensure traffic management plans are understood and followed
Verify worker competency and authorization
Actively observe work and intervene when unsafe conditions exist
Encourage stop-work authority without consequence

## Slide 12
Learning from Incidents
Consider incidents where:
A worker was struck during backing
A pedestrian entered an active equipment zone
A spotter was distracted or improperly positioned
Ask the group:
What safeguards failed?
What could have prevented the exposure?
How do we ensure this doesn’t happen here?
What objects in today’s work area could roll, slide, or fall?

## Slide 13
Field Verification: IOGP Questions & Actions
Hazard Prevention Questions | Prevention Actions
Are there designated routes and segregation between personnel and moving vehicles/mobile equipment in the workplace? Are systems in place to prevent unexpected movement? E.g., parking brakes and wheel chocks. When maneuvering or reversing, can proximity cameras/sensors be used instead of people being in the line of fire? E.g., signaler. Does the driver/operator have a clear view of personnel in the immediate area and understand where the blind spots are? Note the principles for mobile equipment also apply to water | Designated Routes: Clearly mark routes to separate personnel from vehicles. Unexpected Movement: Use parking brakes and wheel chocks. Proximity Technology: Replace signalers with cameras or sensors for reversing and maneuvering. Operator Awareness: Ensure operators have clear visibility and know blind spots. Note the principles for mobile equipment also apply to water vessels, boats, barges, railway rolling stock, and helicopters.
Visit this link for more information: Life-Saving Rules | IOGP
Scroll down to see the publication on Line of Fire

## Slide 14
New Concepts
Review applicable concepts and apply as necessary (see Attachment B for more details):
 | Concept | Description | Applicable? | Comment
1 | Energy Wheel | It is a visual tool used in safety management to help identify, categorize and manage hazards based on the types of energy present in the workplace. It simplifies the hazard recognition process by focusing on the various energy sources that could cause harm if not properly controlled. | Yes | 
2 | Hierarchy of Control | It is a systematic approach used to eliminate or minimize hazards associated with energy sources in the workplace. Part of safety management systems, it is commonly applied in industries where people may be exposed to hazardous energy during the operation, maintenance or servicing of equipment. | Yes | 

## Slide 15
New Concepts
Review applicable concepts and apply as necessary (see Attachment B for more details):
 | Concept | Description | Applicable? | Comment
3 | Stuff That Can Kill You (STCKY) | "Stuff that can kill you" (STCKY) is a safety concept used to identify and manage hazards or conditions in the workplace that pose a significant risk of serious injury or fatality. It emphasizes the importance of recognizing high-risk elements in work environments, which can cause life-threatening, life-altering or life-ending incidents if not properly controlled. | Yes | 
4 | Critical Work | Critical work refers to tasks or activities in a workplace that involve significant risk to people, property or the environment. These tasks often require precise planning, specialized skills and strict safety measures due to the potential for severe consequences if something goes wrong. In essence, critical work involves critical steps with inherent critical risks that could only be managed by critical safeguards. | Yes | 

## Slide 16
New Concepts
Review applicable concepts and apply as necessary (see Attachment B for more details):
 | Concept | Description | Applicable? | Comment
5 | Direct Control | This refers to the proactive and hands-on supervision, intervention and management of work activities to ensure safety standards and protocols are strictly followed. It involves real-time oversight by competent personnel to minimize risks and immediately address any unsafe conditions or behaviours. Direct Controls work even if people make errors. | Yes | Alternative Controls are specifically designed to mitigate human error. When a Direct Control is not feasible, there must be at least two Alternative Controls, from at least two or more of the available categories.
6 | High Energy Control Assessment (HECA) | HECA, also known as energy-based observation, is a structured process used to identify, evaluate and control risks associated with high-energy activities in the workplace. These activities involve significant energy sources — such as mechanical, electrical, chemical or thermal energies — that have the potential to cause catastrophic injuries or damage. HECA ensures that organizations assess and integrate robust safeguards to manage these risks effectively. | Yes | 

## Slide 17
Questions
Where are the mobile equipment line-of-fire hazards on today’s job?
Who is responsible for traffic control and spotter coordination?
What will we do if visibility or conditions change?
How do we confirm communication before equipment moves?

## Slide 18
Final Thoughts
Key Takeaways
Moving equipment and people must be kept apart
Visibility and communication save lives
Line of fire incidents are predictable and preventable
When in doubt—stop, communicate, and reassess
Supporting Materials
Site traffic map
Hand signal reference card
Blind-spot diagrams
Incident case studies
SIMOPS coordination checklist