## Slide 1
Line of Fire Program
Mechanical Lifting / Hoisting Activity Package

## Slide 2
Activity Description
Mechanical lifting and hoisting involve the use of cranes, hoists, winches, forklifts, and other mechanical devices to raise, lower, or move loads. These activities present high-risk exposure to line of fire, dropped objects, load instability, and equipment failure hazards.
This activity package supports safe planning, execution, and supervision of lifting and hoisting tasks.

## Slide 3
Why This Matters
Mechanical lifting incidents can result in:
Serious injury or fatality from falling or swinging loads
Crushing injuries from pinch points
Structural failure due to overloading or improper rigging
Equipment damage and dropped objects
Loss of load control due to wind, ground instability, or system failure
Many lifting incidents are predictable and preventable through planning, competency, and safeguards.

## Slide 4
LoF & DROPS Hazard Categories
This activity aligns with the following ESC hazard categories:
Dropped Objects
Struck-by (swinging or falling load)
Caught-between (load and structure)
Stored Energy Release
Equipment Failure
Uncontrolled Movement

## Slide 5
Common Hazard Scenarios
Standing or walking under a suspended load
Improper rigging or incompatible lifting gear
Exceeding load ratings or ignoring load charts
Poor communication between operator and spotter
Unstable ground or inadequate crane setup
Wind or weather impacts on load control
Unauthorized personnel entering the lift zone

## Slide 6
LoF Injury reduction campaign
You are in the line of fire when you are at risk of coming into contact with a force your body cannot endure.
Mechanical lifting/hoisting awareness is:
Stored Energy Contact with stored energy Includes pressure releases
Striking Hazards Struck by or striking against an object Includes dropped objects
Crushing Hazards Caught in, on or between an object Includes hand injuries

## Slide 7
This overview includes materials that relate to the Line of Fire Life Saving Rule and some that do not. The Life Saving Rule focuses on body positioning.
This rule indicates:
Keep yourself and others out of the line of fire
I position myself to avoid:
  Moving objects
  Vehicles
  Pressure releases
  Dropped objects
I establish and obey barriers and exclusion zones
I take action to secure loose objects and report potential dropped objects
Line of Fire Life Saving Rule

## Slide 8
Related Life Saving Rules
FIT FOR DUTY
BYPASSING SAFETY CONTROLS
SAFE MECHANICAL LIFTING
WORK AUTHORIZATION

## Slide 9
Critical Safeguards
Planning & Authorization
Conduct a lift plan appropriate to task complexity (routine, non-routine, critical lift)
Verify load weight, center of gravity, and lifting points
Obtain required permits and approvals
Define lift zones and exclusion areas
Consider Direct or Alternative Controls
Equipment & Rigging
Use certified lifting equipment and rigging
Inspect slings, shackles, hooks, and hardware before use
Confirm crane/hoist capacity and configuration
Use tag lines to control load movement where required

## Slide 10
Critical Safeguards
People & Competency
Ensure operators and riggers are trained and competent
Assign a designated lift leader
Use qualified signalers/spotters
Confirm everyone understands their role
Execution
Maintain exclusion zones—no one under suspended loads
Lift slowly and smoothly; avoid shock loading
Stop work if conditions change or safeguards are ineffective
Follow hand signals or agreed communication method only

## Slide 11
Responsibilities

## Slide 12
Warning Signs & Red Flags
Missing or damaged electrical covers
Exposed conductors or temporary wiring
Tripped breakers or blown fuses repeatedly
Unlabeled panels or unclear isolation points
Moisture around electrical equipment
People unsure of voltage levels or boundaries

## Slide 13
Field Verification: IOGP Questions & Actions
Hazard Prevention Questions | Prevention Actions
Are unauthorized individuals restricted from entering exclusion/red zones, and are these zones access controlled during lifting and hoisting activities? Have you secured or removed loose objects prior to the lift? Could a load swing when being lifted or lowered? Has rigging equipment been loaded to more than its maximum safe limit? Are approved forklift lifting attachments used instead of free-rigging (direct loading onto the forks)? Are hands free tools used to avoid contact with the load? E.g., tag lines, push pull sticks. | Access Control: Prevent unauthorized access to exclusion/red zones. Use barriers for access control. Secure loose objects: Secure or remove loose objects prior to the lift. Control Excessive Load Movement: Control load swing to prevent unexpected movement during lifting or lowering. Consider proper rigging center of gravity, wind, and motion. Rigging Safety: Use rigging equipment within safe load limits. Proper Attachments: Use approved forklift attachments; no free-rigging. Hands Free Lifting: Use hands free tools to avoid contact with the load. E.g., tag lines, push pull sticks.
Visit this link for more information: Life-Saving Rules | IOGP
Scroll down to see the publication on Line of Fire

## Slide 14
New Concepts
Review applicable concepts and apply as necessary (see Attachment B for more details):
 | Concept | Description | Applicable? | Comment
1 | Energy Wheel | It is a visual tool used in safety management to help identify, categorize and manage hazards based on the types of energy present in the workplace. It simplifies the hazard recognition process by focusing on the various energy sources that could cause harm if not properly controlled. | Yes | 
2 | Hierarchy of Control | It is a systematic approach used to eliminate or minimize hazards associated with energy sources in the workplace. Part of safety management systems, it is commonly applied in industries where people may be exposed to hazardous energy during the operation, maintenance or servicing of equipment. | Yes | 

## Slide 15
New Concepts
Review applicable concepts and apply as necessary (see Attachment B for more details):
 | Concept | Description | Applicable? | Comment
3 | Stuff That Can Kill You (STCKY) | "Stuff that can kill you" (STCKY) is a safety concept used to identify and manage hazards or conditions in the workplace that pose a significant risk of serious injury or fatality. It emphasizes the importance of recognizing high-risk elements in work environments, which can cause life-threatening, life-altering or life-ending incidents if not properly controlled. | Yes | 
4 | Critical Work | Critical work refers to tasks or activities in a workplace that involve significant risk to people, property or the environment. These tasks often require precise planning, specialized skills and strict safety measures due to the potential for severe consequences if something goes wrong. In essence, critical work involves critical steps with inherent critical risks that could only be managed by critical safeguards. | Yes | 

## Slide 16
New Concepts
Review applicable concepts and apply as necessary (see Attachment B for more details):
 | Concept | Description | Applicable? | Comment
5 | Direct Control | This refers to the proactive and hands-on supervision, intervention and management of work activities to ensure safety standards and protocols are strictly followed. It involves real-time oversight by competent personnel to minimize risks and immediately address any unsafe conditions or behaviours. Direct Controls work even if people make errors. | Yes | Alternative Controls are specifically designed to mitigate human error. When a Direct Control is not feasible, there must be at least two Alternative Controls, from at least two or more of the available categories.
6 | High Energy Control Assessment (HECA) | HECA, also known as energy-based observation, is a structured process used to identify, evaluate and control risks associated with high-energy activities in the workplace. These activities involve significant energy sources — such as mechanical, electrical, chemical or thermal energies — that have the potential to cause catastrophic injuries or damage. HECA ensures that organizations assess and integrate robust safeguards to manage these risks effectively. | Yes | 

## Slide 17
Other Considerations
Pre-Task Risk Assessment Checklist
Before starting work, confirm:
☐ Load weight and lift plan are verified
☐ Equipment inspections completed
☐ Ground conditions are stable
☐ Weather/wind conditions are acceptable
☐ Communication methods agreed
☐ Exclusion zones established and enforced
☐ Emergency process designs understood
Human Factors to Watch For
Time pressure leading to shortcuts
Overconfidence in “routine” lifts
Distractions or poor situational awareness
Fatigue affecting judgment
Assumptions instead of verification
Pause if: something doesn’t look or feel right.

## Slide 18
Other Considerations
Stop Work Triggers
Stop the task immediately if:
Load becomes unstable or uncontrolled
Equipment or rigging shows signs of failure
Communication is lost or unclearWeather conditions exceed limits
Unauthorized personnel enter the lift zone
The lift deviates from the approved plan
Learning from Incidents
Common root causes include:
Inadequate lift planning
Improper rigging selection
Failure to control exclusion zones
Standing in the line of fire
Poor supervision or role clarity
Key Lesson:
Mechanical lifting incidents rarely result from equipment failure alone—human and system failures are almost always involved.

## Slide 19
Final Thoughts
Key Takeaways
If it can fall, swing, or shift—it can injure or kill
Never stand under a suspended load
Plan the lift, then lift the plan
Everyone has the authority to stop unsafe lifting work
Mechanical lifting is a team activity—communication is critical