## Slide 1
Line of Fire Program
Objects with Uncontrolled Roll, Slide or Fall Potential Activity Package

## Slide 2
Purpose
To raise awareness of hazards associated with objects that can:
roll,
slide, or
fall unintentionally,
and to provide practical safeguards to prevent:
line-of-fire injuries,
dropped object incidents, and
equipment damage.

## Slide 3
Scope
This activity applies to all work activities where materials, tools, equipment, or components may become unstable due to gravity, vibration, slope, wind, movement, or poor securing.
Applicable across:
Construction and maintenance
Drilling and completions
Production and processing facilities
Warehousing and material handling
Transportation and logistics

## Slide 4
Hazard Description
Objects can become uncontrolled when they are:
Stored or positioned on inclines or uneven surfaces
Stacked, racked, or placed at height
Exposed to vibration, movement, or weather
Poorly secured, restrained, or supported
Impacted by vehicle or equipment movement
Uncontrolled movement can result in:
Struck-by or caught-between injuries
Serious or fatal dropped-object incidents
Damage to equipment and infrastructure

## Slide 5
LoF injury reduction campaign
You are in the line of fire when you are at risk of coming into contact with a force your body cannot endure.
Uncontrolled Roll, Slide or Fall Potential hazards are:
Stored Energy Contact with stored energy Includes pressure releases
Striking Hazards Struck by or striking against an object Includes dropped objects
Crushing Hazards Caught in, on or between an object Includes hand injuries

## Slide 6
This overview includes materials that relate to the Line of Fire Life Saving Rule and some that do not. The Life Saving Rule focuses on body positioning.
This rule indicates:
Keep yourself and others out of the line of fire
I position myself to avoid:
  Moving objects
  Vehicles
  Pressure releases
  Dropped objects
I establish and obey barriers and exclusion zones
I take action to secure loose objects and report potential dropped objects
Line of Fire Life Saving Rule

## Slide 7
Related Life Saving Rules
FIT FOR DUTY
SAFE MECHANICAL LIFTING
WORK AUTHORIZATION

## Slide 8
High-Risk Objects
Potential Consequences
Examples | Potential Consequences
Pipe, casing, tubing, and round stock Pallets, drums, totes, and cylinders Tools, rigging gear, and components at height Materials staged near edges or openings Equipment parts during lifting or maintenance | Fatal or serious injuries (head, torso, crush injuries) Dropped objects striking people below Equipment failure or loss of containment Production downtime and regulatory exposure

## Slide 9
Key Risk Factors
Sloped or uneven ground
Poor housekeeping and congestion
Inadequate blocking, chocking, or restraints
Lack of edge protection or toe boards
Simultaneous Operations (SIMOPS) increasing exposure

## Slide 10
Required Safeguards (Hierarchy of Controls)
Elimination / Substitution
Store materials flat and at ground level where possible
Use engineered storage systems instead of loose stacking
Engineering Controls
Chocks, wedges, cradles, or pipe racks
Toe boards, edge protection, and kick plates
Barriers and exclusion zones below stored materials
Mechanical restraints or tie-downs
Administrative Controls
FLHA identifying roll/slide/fall hazards
Defined stacking and storage standards
Permit requirements for work at height
Clear load-securement process designs
Consider Direct Controls or Alternative Controls
PPE (Last Line of Defense)
Hard hats with chin straps
Safety footwear with toe protection
Gloves appropriate for handling materials

## Slide 11
Responsibilities
Workers
Identify and communicate unstable objects
Never place hands, feet, or body in a line of fire
Secure materials immediately after placement
Stop work if objects appear unstable
Respect exclusion zones and barricades
Supervisors/Leaders
Ensure safeguards are in place before work begins
Verify materials are stored and secured correctly
Reinforce stop-work authority
Monitor SIMOPs and changing conditions
Lead by example in hazard recognition

## Slide 12
Field Verification: IOGP Questions & Actions
Hazard Prevention Questions | Prevention Actions
Are any items or objects that can roll, slide, or fall adequately secured or restrained? E.g., top heavy pipes, steel sheets, items installed/stored at height, trench walls, or transported items. Are exclusion/red zones in place and access controlled where there is potential for drops or uncontrolled movement? E.g., by barriers. Do exclusion/red zones consider dropped objects that could potentially bounce, ricochet, or roll after first impact? Are loads adequately secured before lifting, loading, unloading, or transporting, on land or by water? E.g., transport head boards, side stanchions. Are items to be transported properly packaged to prevent uncontrolled movement? E.g., baskets, cradles, pipe chocks, support saddles, load securing devices. | Secure/Restrain Items: Secure/restrain top heavy objects, pipes, steel sheets, items installed/stored at height, trench walls, or transported items that can roll, slide, or fall. Exclusion/Red Zones: Use barriers to control and prevent unauthorized access, accounting for objects that might fall or bounce. Load Security: Ensure loads are secure before lifting, loading, unloading, or transporting. Packaging for Transport and Storage: Use baskets, cradles, chocks, support saddles, or load securing devices.
Visit this link for more information: Life-Saving Rules | IOGP
Scroll down to see the publication on Line of Fire

## Slide 13
New Concepts
Review applicable concepts and apply as necessary (see Attachment B for more details):
 | Concept | Description | Applicable? | Comment
1 | Energy Wheel | It is a visual tool used in safety management to help identify, categorize and manage hazards based on the types of energy present in the workplace. It simplifies the hazard recognition process by focusing on the various energy sources that could cause harm if not properly controlled. | Yes | 
2 | Hierarchy of Control | It is a systematic approach used to eliminate or minimize hazards associated with energy sources in the workplace. Part of safety management systems, it is commonly applied in industries where people may be exposed to hazardous energy during the operation, maintenance or servicing of equipment. | Yes | 

## Slide 14
New Concepts
Review applicable concepts and apply as necessary (see Attachment B for more details):
 | Concept | Description | Applicable? | Comment
3 | Stuff That Can Kill You (STCKY) | "Stuff that can kill you" (STCKY) is a safety concept used to identify and manage hazards or conditions in the workplace that pose a significant risk of serious injury or fatality. It emphasizes the importance of recognizing high-risk elements in work environments, which can cause life-threatening, life-altering or life-ending incidents if not properly controlled. | Yes | 
4 | Critical Work | Critical work refers to tasks or activities in a workplace that involve significant risk to people, property or the environment. These tasks often require precise planning, specialized skills and strict safety measures due to the potential for severe consequences if something goes wrong. In essence, critical work involves critical steps with inherent critical risks that could only be managed by critical safeguards. | Yes | 

## Slide 15
New Concepts
Review applicable concepts and apply as necessary (see Attachment B for more details):
 | Concept | Description | Applicable? | Comment
5 | Direct Control | This refers to the proactive and hands-on supervision, intervention and management of work activities to ensure safety standards and protocols are strictly followed. It involves real-time oversight by competent personnel to minimize risks and immediately address any unsafe conditions or behaviours. Direct Controls work even if people make errors. | Yes | Alternative Controls are specifically designed to mitigate human error. When a Direct Control is not feasible, there must be at least two Alternative Controls, from at least two or more of the available categories.
6 | High Energy Control Assessment (HECA) | HECA, also known as energy-based observation, is a structured process used to identify, evaluate and control risks associated with high-energy activities in the workplace. These activities involve significant energy sources — such as mechanical, electrical, chemical or thermal energies — that have the potential to cause catastrophic injuries or damage. HECA ensures that organizations assess and integrate robust safeguards to manage these risks effectively. | Yes | 

## Slide 16
Questions & Additional Verifications
Questions
What objects in today’s work area could roll, slide, or fall?
What could cause those objects to move unexpectedly?
What safeguards are in place—and are they adequate?
What will we do if conditions change?
Additional Verification Checklist
☐ Materials chocked, blocked, or restrained
☐ No loose items near edges or openings
☐ Exclusion zones clearly marked
☐ Housekeeping maintained
☐ People aware of roll/slide/fall hazards
Key Message:
If an object can move—it will. Control gravity before it controls the outcome.